## Slide 1: Term project
CA, 2017 Fall
Sang Jun Nam, TA
heesosic@korea.ac.kr

## Slide 2: Overview
Objective: Improvement of cache replacement policy
Source code analysis report 10 pts
Cache
Given
Improved cache replacement policy
Cache hit rate of proposed cache replacement policy
5 pts
More improved cache replacement policy
Proposed cache replacement policy report
10 pts
Cache hit rate of proposed cache replacement policy
5 pts
Due : 12/4 23:59:59
Due : 12/11 23:59:59
Modify
Modify

## Slide 3: 1st term project
Analyze the source code of cache (10 pts)
  You have to understand and analyze the source code of cache in Simplescalar (cache.c, cache.h)
    Main parameters, main functions, etc.
  Submission
    Report (MS word, limitation: 4)
Propose an advanced cache replacement policy (5 pts)
  You have to propose and implement an advanced cache replacement policy in Simplescalar
  Depending on average hit rate of L1 data cache (dl1) and L2 data cache (ul2), score is granted
    Cache hit rate
    The team who has the highest cache hit rate will get 5 points
    The score will be reduced by 0.1 point depending on your rank
      When there are two in second grade, the following team is fourth
  Submission
    Modified source code (cache.c, cache.h)
    Screenshot of execution result
Due date: 12/4 (Monday) 23:59:59
koreasmrl@gmail.com

## Slide 4: 2nd term project
Propose a more advanced cache replacement policy (15 pts)
  You have to propose and implement a more advanced cache replacement policy in Simplescalar
  You have to submit your proposed cache replacement policy report (10 pts)
    Which scheme is used
  Depending on average hit rate of L1 data cache (dl1) and L2 data cache (ul2), score is granted (5 pts)
    Same as 1st
  Submission
    Modified source code (cache.c, cache.h)
    Proposed cache replacement policy report (MS word, limitation: 2)
    Screenshot of execution result
Due date: 12/11 (Monday) 23:59:59
koreasmrl@gmail.com

## Slide 5: Cache parameters
L1 Data Cache (dl1)
  Number of sets in the cache 64
  Block size of the cache 32
  Associativity of the cache 8
L2 Data Cache (ul2)
  Number of sets in the cache 512
  Block size of the cache 64
  Associativity of the cache 8
Other Cache
  Number of sets in the cache: (default)
  Block size of the cache: (default)
  Associativity of the cache: (default)

## Slide 6: Notice
How to measure cache replacement policy
  As benchmark, you have to use applications below
    apsi
    mcf
  You have to use Simplescalar source code and configuration, decided by TA
    Configuration – default values
    Don’t modify Simplescalar source code and configuration except for things related to cache replacement policy
※ Remember!
    If you use other benchmarks, or modify configuration except for cache replacement policy, you will get 0 point
Two people per a team
  You have to look for your partner
  It doesn’t matter, if you do alone (but, providing no benefit)
  Send me an e-mail about partner until 11/27 (Monday)
    koreasmrl@gmail.com
About late submission
  Report
    2 points are subtracted within a week from the due date
    After a week, 0 point is granted
  Others
    After the due date, 0 point is granted

## Slide 7
Q&A